## Slide 1: Invyswell: A Hybrid Transactional Memory for Haswell’s Restricted Transactional Memory
PACT 2014
Paper Reading (schedule):
April 24, 2015, Satoshi Matsushita
Authors:
Irina Calciu, Brown Univ. http://cs.brown.edu/~irina/
Justin Gottschlich, Intel labs : http://justingottschlich.com/
Tatiana Shpeisman, Intel Labs
Gilles Pokam, Intel Labs
Maurice Herlihy, Brown Univ.: https://cs.brown.edu/people/faculty/mph.html
http://cs.brown.edu/~irina/papers/invyswell.pdf

## Slide 2: Intel Transactional Synchronization Extensions (TSX)
Hardware Lock Elision (HLE)
Restricted Transactional Memory (RTM)
RTM
xacquire lock xchg
prefix
New prefix
xrelease mov mem,reg
Speculative
transactional
execution
HLE
time
Lock variable
xbegin fallback_code
xend
Speculative
transactional
execution
xabort
Cf. http://en.wikipedia.org/wiki/Transactional_Synchronization_Extensions

## Slide 3: TSX: nest, abort
RTM
time
xbegin fallback_code2
xend
xabort imm
xbegin fallback_code1
xend
fallback_code1:
fallback_code2:
(imm, state) -> EAX

## Slide 4: RTM: Restrictions
L1 Cache (32KB 8-assoc.) for transactional state store: need one cache line for ether read_set, or write_set
Aborted by state buff full, interrupt, context switch
Certain (uncommon) instr.s always cause abort
No forward progress guaranteed
No escape actions
Cf. http://www.hpts.ws/papers/2013/HTM.pdf

## Slide 5: The paper..
Resolve limitation of RTM with Software and Hardware hybrid Transactional Memory (TM)
Due to ‘no escape’ RTM limitation, trying five TM strategies in sequence.
No crash, no fault tolerance
  Higher performance with 5 strategies
    SpecSW is closer to so called transaction. It consults Contention Manager for commit decision.
  Simple commit with lock, considering lower impact to concurrently running RTM transaction
Modification of InvalSTM (software TM by the co-auther Gottschlich) to make it HTM hybrid.

## Slide 6: Invyswell Design
Hardware TM: LWHW(small Tx), BMHW
Software TM: SpecSW, IrrevocSW (always commit), SglSW (Giant lock)
Bloom Filter for
Conflict detection
Giant lock
r/w
write
read/write

## Slide 7: Bloom filter
False positive matches are possible, but false negatives are not
  A strong space advantage: 1% error with ~9.6 bits/element. Additional ~4.8 bits/elem. reduces ~1% false-positive rate
  O(k) for add items or to check
  Can not remove an element
Cf. http://en.wikipedia.org/wiki/Bloom_filter

## Slide 8: Optimization in specSW
Avoiding abort of inflight HW transaction
  Reading lock for inflight transaction list aborts hardware transactions (RTM)
  Using slotted array to eliminate lock in linked list
Reducing conflict
  Changing commit order
    Lock -> commit -> invalidate -> unlock
    Recording read location in bloom filter if the read is not in write-set (RAW, True dependency: http://en.wikipedia.org/wiki/Data_dependency)
Other optimizations discussed in section 6.
  Fail-Fast mode with priority, read-only transaction

## Slide 9: Bug in RTM HW Sandboxing (Sec. 5.2)
“loop-hole”, an unlikely sequence of events in which
  (1) mutually inconsistent reads cause a spurious memory write,
  (2) which overwrite an address later used as the target of an indirect jump in that same transaction,
  (3) thereby causing a jump to a location that happens to contain either an _xend (commit transaction) instruction, or immediate data that looks like one.
  Executing this instruction without the final commit lock check could prematurely commit an inconsistent set of changes
Solution:
  Check the commit_lock before doing an indirect jump (hand code)
  No indirect jumps: also preventing buffer overflow vulnerability

## Slide 10: Conclusion
Architecture researches sometimes direct to a brute forth or a combination of existing solution.
They may seem to show presence in evaluation of improvement in benchmarks, instead of proposing a novel algorithm. … 5% Club …
I think it is due to they do not want to change the important component ‘CPU, or LSI Chip’. Some have been trying it, ending with ‘Pie in the Sky’, except ones eventually introduced in real LSI.

## Slide 11: References (except ones inline)
Haswell microarchitecture: http://en.wikipedia.org/wiki/Haswell_%28microarchitecture%29
Intel Haswell TSX page: https://software.intel.com/en-us/blogs/2012/02/07/transactional-synchronization-in-haswell
Haswell instruction set manual: https://software.intel.com/sites/default/files/m/9/2/3/41604
An Efficient Software Transactional Memory Using Commit-Time Invalidation, Justin E. Gottschlich, et.al:http://justingottschlich.com/content/cgo10_inval.pdf
An Evaluation of Intel’s Restricted Transactional Memory for CPAs: https://kar.kent.ac.uk/36939/1/9780956540973_020.pdf
Radix Tree: http://en.wikipedia.org/wiki/Radix_tree
Apaptive Radix Tree: ARTful http://www3.informatik.tu-muenchen.de/~leis/papers/ART.pdf