## Slide 1: Low-Latency Datacenters
John Ousterhout Platform Lab Retreat May 29, 2015

## Slide 2: Datacenters: Scale and Latency
Scale:
  1M+ cores
  1-10 PB memory
  200 PB disk storage
Latency:
  < 0.5 µs speed-of-light delay
Most work so far has focused on scale:
  One app, many resources
  Map-Reduce, etc.
Latency potential unrealized:
  High-latency hardware/software
  Most apps designed to tolerate latency (communication via large blocks)

## Slide 3: Latency
Round-trip times (100K servers):
  Today: 100-500 µs best case
  Often much worse because of congestion
  Hardware limit: ~2 µs
Storage latency dropping:
  Disk → Flash → DRAM
Can we create a new platform that makes the hardware limit accessible to applications?
If so, will it enable important new applications?

## Slide 4: Clean-Slate Low-Latency Datacenter
New switching architecture (30 ns per switch)
NIC fused with CPU cores; on-chip routing
User-level networking, polling instead of interrupts
New transport protocol
Storage systems based primarily in DRAM
New software stack

## Slide 5: Low-Latency Storage: RAMCloud
New class of datacenter storage:
  All data in DRAM at all times (disk/flash for backup only)
  Large scale: aggregate 1000’s of servers
  Low latency: 5-10µs remote access
1000x improvements over disk in
  Performance
  Energy/op
Goal: enable a new class of data-intensive applications
Master
Backup
Master
Backup
Master
Backup
Master
Backup
…
Appl.
Library
Appl.
Library
Appl.
Library
Appl.
Library
…
Datacenter Network
Coordinator
1000 – 100,000 Application Servers
1000 – 10,000 Storage Servers
32-256 GB per server

## Slide 6: New Transport Protocol
TCP protocol optimized for:
  Throughput, not latency
  Long-haul networks (high latency)
  Congestion throughout
  Modest # connections/server
Future datacenters:
  High performance networking fabric:
    Low latency
    Multi-path
  Congestion primarily at edges
    Little congestion in core
  Many connections/server (1M?)
Need new transport protocol
Top-of-rack switches
Congested link
“Perfect” core fabric

## Slide 7: New Transport Protocol, cont’d
Greatest obstacle to low latency:
  Congestion at receiver’s link
  Large messages delay small ones
Solution: drive congestion control from receiver
  Schedule incoming traffic
  Prioritize small messages
Behnam Montazeri will present work in progress

## Slide 8: Low-Latency Software Stacks?
Today’s stacks: highly layered
Good for structuring software
  Each layer solves one problem
Bad for performance
  Each layer adds latency
Example: Thrift RPC system
  Handles several problems: marshalling, threading, etc.
  General-purpose: re-pluggable components
  Adds 7 µs latency
For low latency, must replace the entire software stack

## Slide 9: Reducing Software Stack Latency
High
Latency
1. Optimize layers (specialize?)
2. Eliminate layers
3. Bypass layers

## Slide 10: Integrate NIC Into CPU Chip?
Core
Switch
Network
Per-Core
Mini-NIC
OS controls routing tables for incoming packets
Core
Core
Core
Core
Core
Core
Core

## Slide 11: Low Latency => New Applications?
Does 2 µs latency matter?
Use low latency for collecting data?
  Small chunks of data
  Random access
  Dependencies serialize accesses
  Need a lot of chunks in a small amount of time:
    20K chunks in 50 ms?
Use low latency for new computational models?
  Independent compute-storage elements
  Low latency allows high coherency

## Slide 12: Discussion Topics
What are the key elements of a low-latency platform for datacenters?
What will a new software stack look like?
What applications could make use of a low-latency datacenter?

## Slide 13: Palette