## Slide 1: Fast Crash Recovery in RAMCloud
Ryan Stutsman
SEDCL Retreat
June 3, 2011

## Slide 2: Durability and Availability
Goals:
  No impact on performance
  Minimum cost, energy
Replicate in DRAM of other masters?
  3x system cost, energy
  Still have to handle power failures
  Replicas unnecessary for performance

## Slide 3: Durability and Availability
RAMCloud approach:
  1 copy in DRAM
  Backup copies on disk/flash: durability ~ free!

## Slide 4: Problems
Synchronous disk I/O’s during writes?
  Buffered logging
Data unavailable after crashes?
  Fast recovery

## Slide 5: RAMCloud Architecture
Master
Backup
Master
Backup
Master
Backup
Master
Backup
…
Appl.
Library
Appl.
Library
Appl.
Library
Appl.
Library
…
Datacenter Network
Coordinator
1,000 – 10,000 Storage Servers
1,000 – 100,000 Application Servers
Storage Servers act as both a Master and a Backup

## Slide 6: Buffered Logging
Notes: Incoming data is appended to an in-memory log which is replicated among backups.
The in-memory log is broken into 8 MB pieces called “segments”.
Once a master fills a segment it is never modified again.
Backups buffer just the most recent segment, whenever the master fills a segment it notifies the backups that it is done with that segment.
The backups begin to flush that segment out to disk.
Masters then notify the backups that they would like to write another segment, the backups reserve buffer space for that segment and the process repeats.
After 3 backups have buffered the data for an update the master updates its hash table and returns “success” to the client.
At that point the client can expect, come hell or high water, that the object will be reflected on all future read requests.
This means that the backups need to guarantee updates to their buffered replica’s of the masters segment durable.
Do provide this we expect backups to have a small amount of non-volatility they use to make this guarantee.
This allows us to have updates on the order of 2xRPC RTT (10 us) rather than 4-8 ms.

## Slide 7: Buffered Logging
No disk I/O during write requests
  But must guarantee buffered data durability:
    DIMMs with built-in flash backup?
    Caches on enterprise disk controllers?
    Per-server battery backups?
8 MB I/Os minimize disk latency overhead
  Achieves 90% disk bandwidth
  Helpful for reading during fast recovery as well
Master’s memory also log-structured
  Log cleaning ~ generational garbage collection

## Slide 8: Master Crash Recovery
Problem: Data unavailable after a master crash
Goal: 1 – 2 second recovery
  Applications just see “hiccups”
  Good enough for “continuous availability?”
Solution: Harness system scale

## Slide 9: Recovery, First Try
Master chooses backups statically
  Each backup stores entire log for master
Crash recovery:
  Choose recovery master
  Backups read log info from disk
  Transfer logs to recovery master
  Recovery master replays log
First bottleneck: disk bandwidth:
  64 GB / 3 backups / 100 MB/sec/disk ≈ 210 seconds
Solution: more disks (more backups)
Recovery Master
Backups

## Slide 10: Recovery, Second Try
Scatter logs:
  Each log divided into 8MB segments
  Master chooses different backups for each segment (randomly)
  Segments scattered across all servers in the cluster
Crash recovery:
  All backups read from disk in parallel
  Transmit data over network to recovery master
Recovery Master
~1000 Backups

## Slide 11: Scattered Logs
Disk no longer a bottleneck:
  64 GB / 8 MB/segment / 1000 backups ≈ 8 segments/backup
  100 ms/segment to read from disk
  0.8 seconds to read all segments in parallel
Second bottleneck: NIC on recovery master
  64 GB / 10 Gbits/second ≈ 60 seconds
  Recovery master CPU is also a bottleneck
Solution: more recovery masters
  Spread work over 100 recovery masters
  64 GB / 10 Gbits/second / 100 masters ≈ 0.6 seconds

## Slide 12: Recovery, Third Try
Divide each master’s data into partitions
  Recover each partition on a separate recovery master
  Partitions based on tables & key ranges, not log segment
  Each backup divides its log data among recovery masters
Recovery Masters
Backups
Dead Master

## Slide 13: Start of Recovery
Coordinator C gets “M is down” report
C verifies M is down
C broadcasts to cluster: “which segments do you have for M?” “begin reading and partitioning them”
C verifies no segments are missing
C notifies selected recovery masters: “recover this partition of M from these locations”

## Slide 14: Recovery

## Slide 15: Parallelism During Recovery
Tightly overlapped and pipelined
  Each recovery master can recover 400-800 MB of log per second
  All steps are all being performed by all hosts simultaneously
Segments can be replayed in any order
  Possible due to version number on objects
  Recovery masters can work independently and distribute load over backups
  Recovery masters can replay any data when it becomes available

## Slide 16: Recovery Scalability
1 master
6 backups
6 disks
600 MB
11 masters
66 backups
66 disks
6.6 GB

## Slide 17: TODO
Restoring locality
Recovering Backups
Cold boot

## Slide 18: Recovering Backups
In parallel with master recovery
Each master recreates any segments it has stored on that backup elsewhere
Expect to re-replicate 8 segments
  1,000 machines, 64 GB per master
  Just need to buffer on a new backup
  Fast compared to master recovery

## Slide 19: Recovery Summary
Before Crash
Scatter log data
Balance partitions
  Steve’s talk
On Crash
Detect failure
Find log data
Check log integrity
Select new masters
Replay log data
Recreate backups

## Slide 21: Recovery Summary
Before Crash
Scatter log data
Balance master load
  Steve’s talk
On Crash
Detect failure
Find log data
Check log integrity
Select new masters
Replay log data
Recreate backups

## Slide 22: Distribute Segments
To different failure domains
  Each segment should be in a different rack
“Evenly” for fast recovery
  Lower-bound is the time for all disks to read
Without overruning non-volatile buffers
  Need to balance rate as well as total data
Without centralized coordination

## Slide 23: Random Placement
Doesn’t handle failure domain constraints
Somewhat evens data for fast recovery
  Place balls randomly into bins; max expected in any one bin? Not great. (log n / log log n)
Somewhat evens non-volatile buffers load
No centralized coordination

## Slide 24: Random Placement
Best Case Read Time: (20 / 4) * 100 ms = 500 ms
Expected Read Time: max(7,7,2,4) * 100 ms = 700 ms
Time Over Optimal: 200 ms
Minimizing variance between backup is important.

## Slide 25: Random With Refinement
On “segment open”
  Choose 5 candidate backups that meet placement constraints
  Select the one with
    Either, the fewest segments from this master
    Or, the one expected to spend the least amount of time loading recovery data if this master crashed (important when backup performance is heterogeneous)

## Slide 26: Random With Refinement

## Slide 27: Random With Refinement

## Slide 28: Random With Refinement

## Slide 29: Random With Refinement

## Slide 30: Random With Refinement

## Slide 31: Random With Refinement
Best Case Read Time: (20 / 4) * 100 ms = 500 ms
Expected Read Time: max(4,6,6,4) * 100 ms = 600 ms
Time Over Optimal: 100 ms

## Slide 32: Adjust for Disk Speeds
Disk speed varies
When choosing between backups in the random selection choose the host with the least expected time needed to load during recovery

## Slide 33: Random With Refinement
Handles failure domain constraints
Evens data for fast recovery
  Place balls randomly with refinement into bins what is the maximum expected in any one bin? (log log n / log 5)
Somewhat evens non-volatile buffers load
  Hard on “fresh” backups
  Can do something about this if it matters
No centralized coordination

## Slide 34: Scattering Results

## Slide 35: Detecting Incomplete Logs
Problem: Segments may be lost
  With high probability the list is complete
  But, when 3 or more hosts have crashed before segments could be re-replicated
Coordinator checks when receiving segment backup locations
No centralized list of log segments
Solution: Self-describing log
  Check using information in the backup segments

## Slide 36: Log Digests
Each segment includes a log digest
  List of the segment ids that make up the log when the segment was created
After broadcast the coordinator
  Tracks the log digest from the segment with the highest segment id
  Checks to make sure all listed segments have been found among backups

## Slide 37: Finding the Head of the Log
Problem: What if the newest segment was lost?
  Otherwise we might have a stale log digest
Segments have a “head” flag which is cleared when the master is done writing to it
Masters use an “open-before-close” policy
  Prevents the a race between close of a head and open of a new one
If the segment with the highest id is not a “head” then assume data is lost

## Slide 38: Fast Recovery: Strawman #1
Load 64 GB from 3 backups

## Slide 39: Fast Recovery: Strawman #1
Load 64 GB from 3 backups
64 GB / 3 disks / 100 MB/s / disk = 3.5 minutes

## Slide 40: Fast Recovery: Strawman #2
Scatter and load from all (1000) backups
64 GB / 1000 disks / 100 MB/s / disk = 0.6 s
…

## Slide 41: Fast Recovery: Strawman #2
Scatter and load from all (1000) backups
64 GB / 10 Gbps = 1 minute
…

## Slide 42: Fast Recovery
Scatter and load from all (~1000) backups
Partition data among many (~100) replacements
0.6 s by using many disks/NICs
…
Crashed
Master

## Slide 43: Recovery Time Variance
Chart: Cumulative Percent of Recovery Time

## Slide 44: Partitioning Recovery
Coordinator divides up <table, object id> ranges among recovery masters
Minimizing recovery time is difficult
  Must “balance” work among recovery masters
Each master leaves a will behind with the Coordinator

## Slide 45: Message Overheads at Scale

## Slide 46: The Will & Partitions
1, 192
1, 382
3, 18
3, 993
1, 11
2, 99
Table ID | Start Object ID | End Object ID | Partition
1 | 0 | 999 | 
2 | 0 | 999 | 
3 | 0 | 999 | 

## Slide 47: The Will & Partitions
1, 192
1, 382
3, 18
3, 993
1, 11
2, 99
Table ID | Start Object ID | End Object ID | Partition
1 | 0 | 100 | 
2 | 0 | 999 | 
3 | 0 | 999 | 
1 | 101 | 999 | 
Repartitioning of segments can happen “after the fact”