## Slide 1: Durability and Crash Recovery for Distributed In-Memory Storage
Ryan Stutsman,
Asaf Cidon, Ankita Kejriwal,
Ali Mashtizadeh, Aravind Narayanan,
Diego Ongaro, Stephen M. Rumble,
John Ousterhout, and Mendel Rosenblum

## Slide 2: RAMCloud Overview
RAMCloud: General purpose storage in RAM
  Low latency: 5 µs remote access
  Large scale: 10,000 nodes, 100 TB to 1 PB
Enable applications which access data intensively
  Access 100 to 1000x times more data
Simplify development of large scale applications
  Eliminate issues that kill developer productivity
    Partitioning, parallelism/pipelining, locality, consistency
Key Problem: RAM’s lack of durability

## Slide 3: Thesis
Large-scale RAM-based storage must be durable and available for applications to gain its full benefits, and it can be made so cost-effectively using commodity hardware.
Solution
  Fast (1 - 2s) crash recovery for availability
  Restoration of durability after crashes
  Survival of massive failures (with loss of availability)

## Slide 4: Durability Requirements
Minimal impact on normal case performance
Remain available during typical failures
Remain durable during massive/correlated failures
No undetected data loss
Low cost, low energy
  Use commodity datacenter hardware available in a few years
The performance of RAM-based storage
with durability of traditional datacenter storage

## Slide 5: Outline
Master Recovery
Backup Recovery
Massive Failures/Cluster Restart
Distributed Log
  Key structure underlying RAMCloud

## Slide 6: RAMCloud Architecture
Master
Backup
Master
Backup
…
App
Library
App
Library
App
Library
App
Library
…
Datacenter Network
Coordinator
Up to 10,000 Storage Servers
Up to 100,000 Application Servers
Master
Backup
Master
Backup
Masters expose RAM as Key-Value Store
Backups store data from other Masters

## Slide 7: Normal Operation
Master
Backups
In-memory Log
Buffer
Buffer
Buffer
write

## Slide 8: Normal Operation
Master
Backups
In-memory Log
Buffer
Buffer
Buffer
write

## Slide 9: Normal Operation
Master
Backups
Backups buffer update
  No synchronous disk write
  Must flush on power loss
In-memory Log
Buffer
Buffer
Buffer
write

## Slide 10: Normal Operation
Master
Backups
Backups buffer update
  No synchronous disk write
  Must flush on power loss
In-memory Log
Buffer
Buffer
Buffer

## Slide 11: Normal Operation
Master
Backups
Backups buffer update
  No synchronous disk write
  Must flush on power loss
Bulk writes in background
In-memory Log
Buffer
Buffer
Buffer

## Slide 12: Normal Operation
Master
Backups
Backups buffer update
  No synchronous disk write
  Must flush on power loss
Bulk writes in background
Pervasive log structure
  Even RAM is a log
  Log cleaner
In-memory Log
Buffer
Buffer
Buffer
Segment
Replicas

## Slide 13: Normal Operation
Master
Backups
Backups buffer update
  No synchronous disk write
  Must flush on power loss
Bulk writes in background
Pervasive log structure
  Even RAM is a log
  Log cleaner
Hashtable, key → location
In-memory Log
Buffer
Buffer
Buffer
Hashtable

## Slide 14: Normal Operation Summary
Cost-effective
  1 copy in RAM
  Backup copies on disk/flash: durability ~ free!
Fast
  RAM access times for all accesses
  Avoids synchronous disk writes
Non-volatile buffers
Unavailability on crash

## Slide 15: Fast Crash Recovery
What is left when a Master crashes?
  Log data stored on disk on backups
What must be done to restart servicing requests?
  Replay log data into RAM
  Reconstruct the hashtable
Recover fast: 64 GB in 1-2 seconds

## Slide 16: Recovery Bottlenecks
One machine cannot recover in 2s
Key to fast recovery:
Use system scale
Recovery Master
Backups
Crashed
Master
Disks: ~500 MB/s aggregate
NIC: ~1 GB/s

## Slide 17: Distributed Recovery
Scatter/read segments across all backups
  Solves disk bandwidth bottleneck
Recover to many masters
  Solves NIC and memory bandwidth bottlenecks
Recovery Masters
Backups
Crashed Master

## Slide 18: Results
60 Recovery Masters
120 SSDs: 31 GB/s
Recovered: 35 GB
2x270 MB/s SSDs, 60 machines

## Slide 19: Key Issues and Solutions
Maximizing concurrency
  Data parallelism
  Heavily pipelined
    Out-of-order replay
Balancing work evenly
  Balancing partitions
    Divide crashed master up at recovery time
  Segment scattering
    Random, but bias to balance disk read time
Avoiding centralization
  Finding segment replicas
  Detecting incomplete logs

## Slide 20: Backup Recovery
Failures result in loss of segment replicas
Recreate replicas to maintain desired redundancy
  Simple: Master uses same procedure as normal operation
  Efficient: Use master’s in-memory copy
  Concurrent: Work is divided up among all the hosts
B17
B91
Segment 1
B31
B1
B72
Segment 2
Replicas
Master
Segment 3
B68
B68
B12

## Slide 21: Expected Backup Recovery Time
Backup could have 192 GB of data
  1000 64 GB masters triplicating segments
Aggregate network bandwidth: 1000 GB/s
Aggregate disk bandwidth: 200 GB/s
~200 ms if backups have buffer space
~1,000 ms if not
Notes: 80 masters with 64 GB of data triplicated across 80 backups
  Assume 2 x 150 MB/s SSDs
  ~8.2 s (192 GB / (2 x 150 MB/s))
  Each master has ~24 replicas on a given backup

## Slide 22: Massive Failures/Cluster Restart
Unavailability ok during massive/complete outages
  Remain durable
Simplicity is the goal
  Massive failures are expected to be rare
  Shortest restart time is a non-goal (within reason)
Reuse master/backup recovery
  Must make them work correctly under massive failure
Treat massive failure as a series of single failures
Notes: Took 30 mins to get here.

## Slide 23: Massive Failures/Cluster Restart
Must readmit replicas to cluster after mass failure
  All master data is lost
  Only replicas on backups’ disks persist
Start recovery when complete log becomes available
  Determine if recovery can proceed as backups rejoin
Masters
Backups

## Slide 24: Key Issues
Replica garbage collection
  Dilemma when a replica rejoins the cluster
    It may be needed for a recovery
    It may be redundant; master has created new replicas

## Slide 25: Fault-tolerant Distributed Log
Distributed log
  Fast durability in normal case
  Restores availability quickly during crashes
  Clear strategy for maintaining durability
We’ve talked about how the log operates on a good day
Massive Failures
Fast Master Recovery
Distributed Log
Backup Recovery

## Slide 26: Potential Problems
Detecting incomplete logs
  Has a complete log been found for recovery?
Replica consistency
  How are the inconsistencies due to failures handled?

## Slide 27: Finding Replicas
Log segments created/destroyed rapidly across cluster
  100,000s per second
Centralized log information too expensive
  No centralized list of segments that comprise a log
  No centralized map of replica locations
Broadcast on Master crash
  Coordinator contacts each backup explicitly
  Have to contact all backups anyway
    Master’s segments are scattered across all of them
  Collects a list of all available replicas

## Slide 28: Detecting Incomplete Logs
Problem: Ensure complete log found during recovery
  What if all replicas for some segment are missing?
Solution: Make log self-describing
  Add a “log digest” to each replica when it is allocated
  Lists all segments of the log
Reduces problem to finding the up-to-date log digest
S7
S19
S20
[S7, S19, S20]
Digest

## Slide 29: Choosing the Right Digest
Solution: Make most recent segment of log identifiable (the “head”)
  Segments are allocated in an “open” status
  Mark “closed” when head segment fills up
  Only use digests from head segment on recovery
Challenge: Safe transition between log heads

## Slide 30: Preventing Lost Digests
Problem: Crash during head transition can leave no log head
Segment 19
Segment 20
[7, 19]
[7, 19]
Open
Closed
Open
Time
[7, 19]
[7, 19, 20]
Closed
Digest
Digest

## Slide 31: Preventing Lost Digests
Problem: Crash during head transition can leave no log head
Segment 19 no longer head, segment 20 hasn’t been created
Segment 19
Segment 20
[7, 19]
[7, 19]
Open
Closed
Open
[7, 19]
[7, 19, 20]
Closed
Digest
Digest
Time
Crash

## Slide 32: Preventing Lost Digests
Solution: Open new log head before closing old one
Segment 19
Segment 20
[7, 19]
Open
Open
[7, 19]
[7, 19, 20]
Closed
Digest
Digest
Open
[7, 19, 20]
[7, 19]
Open
Time

## Slide 33: Inconsistent Digests
Problem: Crash during transition can leave two log digests
Solution: Don’t put data in new head until the old head is closed
  If new log head has no data either is safe to use
Segment 19
Segment 20
[7, 19]
Open
Open
[7, 19]
[7, 19, 20]
Closed
Digest
Digest
Open
[7, 19, 20]
[7, 19]
Open
Time
Crash

## Slide 34: Replica Consistency
Replicas can become inconsistent
  Failures during (re-)creation of replicas
Must recover even with one only replica available for each segment
Can’t prevent inconsistencies
  Make them detectable
  Prevent recovery from using them
Open segments present special challenges

## Slide 35: Failures on Closed Segments
Problem: Master may recover from a partial replica
Solution: Recreate replicas atomically
Backup considers atomic replica invalid until closed
  Will not be persisted or used in recovery
Segment 19 on Master
Replicas for
Segment 19 on Backups
Time

## Slide 36: Failures on Open Segments
Closed segment solution doesn’t work
Problem: Segment in Master’s RAM is changing
  Lost replica may be useful for recovery one moment
  A moment later it must not be used during recovery
Rare: Expect 3 Masters affected every 30 mins or longer
Segment 19 on Master
Replicas for
Segment 19 on Backups
Write
starts
Write
ends
Time

## Slide 37: Failures on Open Segments
Solution
  Make valid replicas distinguishable (close them)
  Notify coordinator to prevent use of open replicas
Segment 19 on Master
Replicas for
Segment 19 on Backups
Write
starts
Write
ends
Open segment 20, close segment 19
Min Head Id: 20
Update Min Head Segment Id on Coordinator
Time

## Slide 38: Fault-tolerant Distributed Log
Detecting incomplete logs
  Broadcast to find replicas
  Log digest provides catalog of segments
  Head of log ensures up-to-date digest is found
Replica consistency
  Atomic replica recreation for most segments
  Centralized minimum head id invalidates lost replicas
No centralization during normal operation
  Even during transitions between segments

## Slide 39: What’s done
Normal operation
  Low latency 5 µs remote access
Master recovery
  1 - 2 s restoration of availability after failures
Backup recovery
  Durability safely maintained via re-replication
[Fall 2009]
[Fall 2010]
[SOSP 2011]
[Feb 2012]

## Slide 40: What’s left
Massive Failures/Cluster Restart
  Replica garbage collection from backups
  Master recovery on coordinator
    Recoveries which can wait for lost replicas
Experiment with longer-lived RAMCloud instances
  Work out kinks
  Measure/understand complex interactions
    e.g. Multiple recoveries, impact of recovery on normal operation, storage leaks, etc.
Explore strategies for surviving permanent backup failures
[Spring 2012]
[Apr 2012]
[May-June 2012]
[Summer 2012]

## Slide 41: Summary
RAM’s volatility makes it difficult to use for storage
  Applications expect large-scale storage to be durable
  RAMCloud’s durability & availability solve this
RAMCloud provides general purpose storage in RAM
  Low latency with large scale
Enables new applications which access more data
Simplifies development of large scale applications