## Slide 1: What happens when you try to build a low latency NIC?
Mario Flajslik

## Slide 2: Overview
Motivation
Setup
Receive path NIC latency
Transmit path NIC latency
Results
Conclusion

## Slide 3: RAMCloud Overview
Storage for datacenters
1000-10000 commodity servers
64 GB DRAM/server
All data always in RAM
Durable and available
Performance goals:
  High throughput: 1M ops/sec/server
  Low-latency access: 5-10µs RPC
Application Servers
Storage Servers
Datacenter

## Slide 4: Datacenter network topology
Current low latency switches ~600ns
Next generation switches promise ~300ns
. . .

## Slide 5: Test setup
xupv5
FPGA
NIC
ICH
MCH
CPU
RAM
ethernet
PCIe 1.1 x1
DMA
rd/wr
size | latency
64B | 2424 ns
128B | 2808 ns
256B | 3464 ns
512B | 4984 ns
DMA read latencies:

## Slide 6: Receiving packets
Pre-allocate buffers (sk_buff) and give them to the NIC
On packet receive DMA data to the buffer, and notify the CPU
CPU
meta
data
sk_buff
sk_buff
sk_buff
…
RAM
packet in
DMA write
write length
interrupt
NIC

## Slide 7: RX path
PCIe
core
CTRL
length (256ns delay)
TX/RX
MAC 0
MAC 1
MAC 2
MAC 3
other sources

## Slide 8: PCIe RX latency breakdown
128B receive (+16B PCIe header)
PCIe 1.1: 250 MB/s -> 576 ns wire time for 144B
All times in nanoseconds
app
trn_tx
pcie_mim_wr
pcie_mim_rd
wire
0
272
416
746
1156
1322
580
128
560

## Slide 9: Transmitting packets
NIC writes back a flag that the packet has been sent and sk_buff can be deallocated. Data written back is the DMA read latency.
CPU
meta
data
sk_buff
sk_buff
sk_buff
…
RAM
reg write
DMA read
write back
packet out
NIC
rsvd(2)
end(1)
id(5)
size(16)
addr(40)
reg write:

## Slide 10: TX path
PCIe
core
CTRL
TX/RX
MAC 0
MAC 1
MAC 2
MAC 3
MEM
MEM
MEM
MEM

## Slide 11: PCIe RX latency breakdown
app
trn_tx
pcie_mim_wr
pcie_mim_rd
wire
0
128
96
240
272
316
380
446
510
pcie_mim_rd
pcie_mim_wr
app
trn_rx
wire
176
576
752
832
1120
1376
1664
1424
1680
0

## Slide 12: Results
RTT of DMA read from the NIC
Xilinx PCIe core latency (128B) = 2126 ns
Latency = 2000 ns + size * 6 ns
Smaller latency for x8 PCIe
size | latency
64B | 2424 ns
128B | 2808 ns
256B | 3464 ns
512B | 4984 ns

## Slide 13: Evolution of PCI
Experiment done with register DMA reads (4 byte DMA reads)
PCI version | DMA read latency
33 MHz PCI | 324 ns
66 MHz PCI-X | 174 ns
133 MHz PCI-X | 84 ns
PCIe x1 | 2106 ns
PCIe x8 | 252 ns

## Slide 14: PHY & MAC
XAUI is interconnect protocol between virtex-5 and the PHY chip
Given times are for a copper cable
Optical cable times are a little better (~10ns better)
MAC
PHY
PHY
MAC
10G NetFPGA NIC
10G NetFPGA NIC
0 ns
192 ns
403 ns
607 ns
819 ns
XAUI
XAUI
109 ns
83 ns
211 ns
211 ns
83 ns
90 ns

## Slide 15: Conclusion
Current Intel 10G NICs (RX+TX): ~5μs
Current Intel 1G NICs (RX+TX): ~9μs
Infiniband (RX+TX): ~2.2μ
There is room for improvement